## Slide 1
Using LiDAR to Map Eroded Forest Roads in the Lake Champlain Basin, Vermont
Sean MacFaden, Jarlath O’Neil-Dunne, Mary Nealon,* Alexandra Marcucci*
University of Vermont Spatial Analysis Laboratory
*Bear Creek Environmental, LLC
Project funded by the US Department of Agriculture Natural Resources
Conservation Service and the Vermont Ecosystem Restoration Program

## Slide 2: Need
Many Forest Roads and Trails Not Represented in Available GIS Datasets
Erosion From Forest Roads May Contribute to Pollutant Loading

## Slide 3: Opportunity
LiDAR Increasingly Available
Improved Processing Methods
Object-based Image Analysis (eCognition)

## Slide 4: Approach
Automated Mapping Combining OBIA with LiDAR and Other High-resolution Inputs
Export Results to Widely-used Formats
Pilot Sites: Rutland County, Upper Missisquoi

## Slide 5
Original LiDAR Point Cloud

## Slide 6
LiDAR-derived Digital
Surface Model (DEM)

## Slide 7
How to create objects for subsequent analysis?

## Slide 8
DEM-derived Dissection

## Slide 9
DEM-derived Landform

## Slide 10: Automated Feature Extraction (OBIA)

## Slide 11: Modeling Approach - Roads
Step 1: Segment
Step 2: Preliminary Selection
Step 3: Connect Fragments
Step 4. Reduce False Positives
Step 5. Final Classification

## Slide 12: Step 1 – Segment

## Slide 13
Segment by Dissection and Landform

## Slide 14: Step 2 – Identify Candidate Roads

## Slide 15
Initial Classification

## Slide 16
Initial Set of Candidate Roads

## Slide 17: Step 3 – Connect Fragments

## Slide 18
Connect Nearby Segments

## Slide 19: Step 4 – Reduce False Positives

## Slide 20
Identify Streams

## Slide 21: Step 5 – Final Classification

## Slide 22
Final Classification – Primary

## Slide 23
Final Classification – Secondary

## Slide 24
Final Classification – Other

## Slide 25: Modeling Approach – Erosion Hotspots
Step 1: Calculate Stream Power Index
Step 2: Segment Roads by SPI
Step 3: Fill Gaps and Consolidate
Step 4. Incorporate Soils Data (K)
Step 5. Classify

## Slide 26
Calculate SPI
SPI = LN((Flow Accumulation)+0.001)
*(Slope/100+0.001))

## Slide 27
Segment by SPI

## Slide 28
Fill Gaps and Consolidate

## Slide 29
Add K Factor from SSURGO
K Factor = 0.32

## Slide 30
Erosion Hotspot Classification
High Risk
Moderate Risk
Low Risk

## Slide 31: GIS Output

## Slide 35: Accuracy Assessment

## Slide 37
Alex Marcucci

## Slide 38
 | Field-verified Roads |  | Modeled Roads (July 2016) |  |  | Modeled Roads (Final – August 2017) |  | 
Parcel | Number | Length (m) | Number | Length (m) | % Capture | Number | Length (m) | % Capture
1 | 24 | 12,111 | 9 | 1,565 | 13% | 15 | 4,085 | 34%
2 | 8 | 4,572 | 6 | 2,578 | 56% | 8 | 3,733 | 82%
3 | 11 | 4,879 | 10 | 1,679 | 34% | 11 | 2,685 | 55%
4 | 13 | 4,335 | 9 | 1,264 | 29% | 12 | 2,309 | 53%
5 | 6 | 4,439 | 6 | 1,877 | 42% | 6 | 2,806 | 63%
Total | 62 | 30,337 | 40 | 8,964 | 30% | 52 | 15,618 | 51%
Roads Classification
Rutland County (0.7-m GSD)

## Slide 39
Roads Classification
Upper Missisquoi (1.6-m GSD)
 | Field-verified Roads |  | Modeled Roads (June 2016) |  |  | Modeled Roads (Final – August 2017) |  | 
Parcel | Number | Length (m) | Number | Length (m) | % Capture | Number | Length (m) | % Capture
1 | 9 | 6,527 | 9 | 3,793 | 58% | 9 | 4,314 | 66%
2 | 20 | 6,514 | 16 | 3,943 | 61% | 17 | 3,878 | 60%
3 | 10 | 2,946 | 6 | 748 | 25% | 3 | 389 | 13%
4 | 5 | 1,929 | 4 | 998 | 52% | 5 | 936 | 49%
5 | 6 | 1,163 | 4 | 211 | 18% | 3 | 137 | 12%
6 | 12 | 3,595 | 2 | 49 | 1% | 2 | 152 | 4%
7 | 2 | 454 | 0 | 0 | 0% | 0 | 0 | 0%
8 | 3 | 985 | 2 | 203 | 21% | 2 | 286 | 29%
9 | 4 | 1,615 | 3 | 209 | 13% | 3 | 147 | 9%
10 | 2 | 392 | 0 | 0 | 0% | 0 | 0 | 0%
11 | 1 | 832 | 1 | 151 | 18% | 0 | 0 | 0%
Total | 74 | 26,951 | 47 | 10,305 | 38% | 44 | 10,239 | 38%

## Slide 40
Erosion Hotspot Classification
Rutland County (0.7-m GSD)
 | Field-verified Erosion Hotspots |  | Modeled Erosion Hotspots (June 2017) |  |  | Modeled Erosion Hotspots (Final – August 2017) |  | 
Site | Number | Length (m) | Number | Length (m) | % Capture | Number | Length (m) | % Capture
4-A | 1 | 45 | 1 | 35 | 77% | 1 | 35 | 79%
4-H | 2 | 55 | 1 | 27 | 49% | 1 | 27 | 49%
4-J | 1 | 47 | 0 | 0 | 0% | 0 | 0 | 0%
4-K | 2 | 101 | 1 | 28 | 28% | 0 | 0 | 0%
4-M | 7 | 141 | 4 | 58 | 41% | 6 | 90 | 64%
5-B | 7 | 209 | 5 | 141 | 67% | 6 | 147 | 70%
5-C | 1 | 10 | 0 | 0 | 0% | 0 | 0 | 0%
5-D | 4 | 183 | 3 | 157 | 86% | 3 | 156 | 85%
5-E | 2 | 87 | 1 | 36 | 42% | 2 | 73 | 84%
5-F | 1 | 129 | 1 | 129 | 100% | 1 | 129 | 100%
Total | 28 | 1,007 | 17 | 611 | 61% | 20 | 658 | 65%

## Slide 41
Erosion Hotspot Classification
Upper Missisquoi (1.6-m GSD)
 | Field-verified Erosion Hotspots |  | Modeled Erosion Hotspots (June 2017) |  |  | Modeled Erosion Hotspots (Final – August 2017) |  | 
Site | Number | Length (m) | Number | Length (m) | % Capture | Number | Length (m) | % Capture
1-B | 2 | 152 | 0 | 0 | 0% | 0 | 0 | 0%
1-C | 1 | 29 | 0 | 0 | 0% | 0 | 0 | 0%
1-E | 1 | 16 | 0 | 0 | 0% | 0 | 0 | 0%
1-F | 2 | 278 | 1 | 94 | 34% | 1 | 104 | 37%
1-I | 6 | 329 | 6 | 226 | 69% | 6 | 236 | 72%
2-A | 1 | 14 | 1 | 14 | 100% | 1 | 14 | 100%
2-C | 2 | 46 | 1 | 26 | 56% | 2 | 46 | 100%
2-D | 1 | 23 | 0 | 0 | 0% | 0 | 0 | 0%
2-H | 1 | 24 | 0 | 0 | 0% | 0 | 0 | 0%
2-I | 1 | 16 | 1 | 16 | 100% | 1 | 16 | 100%
2-J | 1 | 13 | 0 | 0 | 0% | 0 | 0 | 0%
2-N | 1 | 13 | 0 | 0 | 0% | 0 | 0 | 0%
2-V | 2 | 35 | 0 | 0 | 0% | 0 | 0 | 0%
3-B | 1 | 28 | 0 | 0 | 0% | 0 | 0 | 0%
4-D | 2 | 33 | 1 | 18 | 55% | 1 | 18 | 55%
5-D | 2 | 35 | 0 | 0 | 0% | 0 | 0 | 0%
6-B | 1 | 18 | 0 | 0 | 0% | 0 | 0 | 0%
6-C | 1 | 80 | 0 | 0 | 0% | 0 | 0 | 0%
6-J | 3 | 132 | 0 | 0 | 0% | 1 | 18 | 14%
Total | 32 | 1,315 | 11 | 395 | 30% | 13 | 453 | 34%

## Slide 42: Sources of Error
Alex Marcucci

## Slide 43
Line Attenuation

## Slide 44
Alex Marcucci

## Slide 45
Gaps in Road Network

## Slide 46
Missing Erosion Site – No Mapped Road

## Slide 47
Missing Erosion Site – Mapped Road Not Selected

## Slide 48: Phosphorus Loading Estimates

## Slide 49
Volume of Eroded Segments (m3)
Bulk Density Rate – 1,500 kg/m3 (Wemple et al. 2013)
Total P Rate – 250 mg/kg (Wemple et al. 2013)
Apportioned Over 30 Years
Alex Marcucci

## Slide 50
HUC 12 Watersheds

## Slide 51: Lessons
Comprehensive Networks Difficult
Resolution Matters
Eroded Sites Easier to Map
SPI-based Approach Promising
Comparative P Estimates Informative

## Slide 52: Future Research
2-Part Study
Individual Watershed
Refined Automated Modeling
Field Measurements (Road Networks, Site Characteristics, P Estimates for Different Road Types
Alex Marcucci

## Slide 53: Acknowledgments
Matches (CIG, BCE, Cold Hollow to Canada, Pitney Bowes)
Reed Sims, Kip Potter (NRCS)
Beverley Wemple (UVM)
Gary Sabourin, Nancy Patch, Chris Stone, Jim Ryan (VT ANR)
Alex Marcucci

## Slide 54
Using LiDAR to Identify and Map Forest Roads in Trails in Vermont
Sean MacFaden, 802-656-3007, Sean.MacFaden@uvm.edu
Alex Marcucci, 802-223-5140, Alex@BearCreekEnvironmental.com
Jarlath O’Neil-Dunne, 802-656-3324, Jarlath.Oneil-Dunne@uvm.edu
Mary Nealon, 802-223-5140, Mary@BearCreekEnvironmental.com